## Slide 1: Reproducible Evaluation of Pan-Tilt-Zoom Tracking
Gengjie Chen, Pierre-Luc St-Charles,
Wassim Bouachir, Guillaume-Alexandre Bilodeau
LITIV, Polytechnique Montréal
Robert Bergevin,
LVSN - REPARTI, Université Laval

## Slide 2: Background Information
Visual object tracking
  Well studied, plenty of datasets/benchmarks (e.g. VOT)
  Requires no special link between hardware/software
  Only requires “pre-recorded” footage
  Simple evaluation (bounding box in image space)
http://votchallenge.net/vot2014/dataset.html

## Slide 3: Background Information
Visual object tracking… via Pan-Tilt-Zoom cameras
  Algorithm is responsible for camera control (FoV)
  Two-way communication between sensor and algo
  Online/closed-loop problem with time constraints
  Performance depends on response time, hardware
  … biggest problem: evaluation.

## Slide 4: Problem Statement
PTZ tracking evaluation
  Simple fact: camera control = algorithms have unique FoV’s
  Inherently, we cannot rely on pre-recorded footage directly
  Meaning we never have a “common reference” for comparisons
    …otherwise, how can we control all aspects of the test scene?
  Therefore, PTZ experiments are not reproducible.

## Slide 5: Related Works
Only two papers address this issue to our knowledge:
  Qureshi and Terzopoulos (2011)
    Fully controlled 3D virtual world with animated pedestrians
    Limited realism (lighting conditions, resolution, motion blur, etc.)
  Salvagnini et al. (2011)
    Real PTZ camera tracks objects on a calibrated projector screen
    Only provides reproducible experiments “in-lab” (hardware/calib. dependent)
    Limited PTZ operating range

## Slide 6: Proposed Framework
Virtual camera in a real video sequence
  Pre-capture spherical panoramic videos
  Project frames as dynamic texture on virtual sphere
  Virtual PTZ camera defined by controllable view frustum
  Total abstraction for algo (full pan/tilt/zoom support)
PointGrey Ladybug 3

## Slide 7: Proposed Framework
Realistic feedback on control operations
  Simulate camera reorientation delays, network delays
  Consider time lost by algorithm when processing each frame
  Use angular rotation speeds based on real PTZ camera model
Overall, this means:
  Time factor is primordial, and has to be considered.
  Method has to be approximate/fast, or robust/intelligent.

## Slide 8: Proposed Dataset
Tracking sequences
  36 sequences taken from three different panoramic video sessions
  Each sequence is a few seconds to one or two minutes
  Two indoor environments with varied capture conditions
Multiple challenges
  Like VOT categories
  Motion Blur, Scale Change, Out-of-Plane Rotation, Fast motion, Cluttered Background, Illumination variation, etc.

## Slide 9: Proposed Dataset
“Reprojectable groundtruth”
  Each bounding box encodes camera orientation & width/height
  Bounding boxes are unprojected, realigned, reprojected as required

## Slide 10: Proposed Dataset
Example of close-up sequences (boxes are groundtruth)

## Slide 11: Baseline Experiments
Need evaluation metrics for:
  Tracking accuracy
  Camera control performance
In the end, we rely on:
  Center Location Error (CLE) (tracking accuracy)
  Overlap Ratio (OR) (tracking accuracy)
  Target to Center Error (TCE) (camera control)
  Track Fragmentation (TF) (camera control)

## Slide 12: Baseline Experiments
For now, “baseline” set using Camshift (Bradsky, 1998)
Simple strategy, decent results
  Fast tracking & decision making, but not very robust

## Slide 13: Baseline Experiments
Updated arXiv version with extended results coming soon!
  CSK, KCF, SPOT, STRUCK…
 | CSK | KCF | STRUCK | CamShift
Full Dataset | 105.3 | 101.0 | 43.5 | 83.2
CENTER LOCATION ERROR (Pixels)
 | CSK | KCF | STRUCK | CamShift
Full Dataset | 0.311 | 0.235 | 0.331 | 0.317
OVERLAP RATIO

## Slide 14: Conclusion
We solve the PTZ tracking reproducibility problem
Our approach relies on real footage, realistic camera model
We consider real time constraints and processing delays
We offer baseline results for you to compare with

## Slide 15: Conclusion
Start benchmarking now!
Detailed version:
http://arxiv.org/abs/1505.04502
C++ framework (based on OpenCV/OpenGL) soon available online:
https://www.polymtl.ca/litiv/vid/