## Slide 1: RippleFPGA: A Routability-Driven Placement for Large-Scale Heterogeneous FPGAs
Chak-Wa Pui, Gengjie Chen, Wing-Kai Chow, Ka-Chun Lam, Jian Kuang,
Peishan Tu, Hang Zhang, Evangeline F. Y. Young, Bei Yu
CSE Department, Chinese University of Hong Kong, Hong Kong
Speaker: Jordan, Chak-Wa Pui

## Slide 2: Outline
Background
Problem Formulation
Algorithms
Experimental Results

## Slide 3: Introduction
As the scale of FPGA grows rapidly, routability becomes a major problem in FPGA placement
The complex architecture of heterogeneous FPGAs yields more sophisticated placement techniques
Architecture sample of heterogeneous FPGA

## Slide 4: Previous Works
Three major categories
  Simulated annealing based, e.g. VPR
  Partitioning-based, e.g. [1]
  Analytical approach, e.g. [2][3]
Limitations of previous works
  Very few of recent works considering routability
  Previous works mainly consider routability in packing
  Most of previous works on heterogeneous FPGAs pack logic elements into CLB and seldom change them after packing
[1] Timing-driven partitioning-based placement for island style FPGAs. TCAD2006
[2] Analytical placement for heterogeneous FPGAs. FPL2012
[3] An efficient and effective analytical placer for FPGAs. DAC2013.

## Slide 5: Contributions
A framework for heterogeneous FPGA flat placement
Several methods are proposed to reduce routing congestion
  Partitioning
  Multi-stage congestion-driven global placement
  Alignment-aware detailed placement

## Slide 6: Problem Formulation
Routability-driven FPGA placement
  Given the netlist and architecture of an FPGA
  Minimize: routed wirelength measured by VIVADO
  Subject to: each logic element has no overlap, no violation to the architecture specific legalization rules

## Slide 7: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 8: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 9: Partitioning
Motivation
  Unbalance between width and height of the chip
  Cannot be resolved by spreading but by reallocating
Comparison of different methods in solving congestion
(c)reallocation
(b)spreading
(a)origin

## Slide 10: Partitioning
Solution:
  Partition the circuit into sub-circuits using recursive bi-partitioning
    Cluster size less than 25% of #cells, cut size less than 5% of #net
  Reallocate the cells across the chip as sparse as we can
    Maintain relative order of clusters and cells inside the same cluster
    Give more space for the cells in spreading while not increase the HPWL too much
cluster1
cluster2
(c)reallocate
(b)clustering
(a)origin

## Slide 11: Partitioning
Effect on real test case
Comparison of spreading result w/o and with partitioning
(b)with partitioning
(a)w/o partitioning

## Slide 12: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 13: Packing
Short global placement
Forming basic logic elements(BLEs) that consist of only one LUT and at least one FFs
Let the remaining LUTs and FFs be BLEs of itself only
Merging two BLEs into one if their LUTs have many connections
(a)
(b)
(c)
(d)
(e)
(f)
(g)
Different type of basic logic elements (BLEs)
LUT
FF
BLE

## Slide 14: Packing
Use maximum weight matching in stage2, weight proportional to distance, only connected LUTs and FFs have edges
In stage3, let the remaining LUTs and FFs be BLEs of itself only
How we do packing in stage2,3
1
3
5
8
2
4
6
7
10
0
9
11
0
1
2
3
4
5
6
7
8
9
10
11
Stage 2

## Slide 15: Packing
Use maximum weight matching in stage4, weight proportional to distance and connections between the LUTs of the vertices
0
1
2
5
3
4
Stage 3
How we do packing in stage4
1
3
5
8
2
4
6
7
10
0
9
11
1
2
4
8
3
7
6
5
0
7
8
6

## Slide 16: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 17: Global Placement
Quadratic placement based on Ripple
Three-stage Optimization
  First two stages, optimize wirelength, fix DSP/RAM to their legal position after stage 1
    Legalizing DSP/RAM disturbs the global placement result a lot
  The third stage optimize routability using inflation (Accumulative)
Same displacement, difference in HPWL
Large displacement

## Slide 18: Global Placement
Routing congestion estimation
  Probabilistic model
  Consider both bounding box and HPWl
#G-Cell
#G-Cell

## Slide 19: Routing congestion estimation
Comparison of the routing congestion estimation obtained by VIVADO and us
(a)VIVADO
(b)Ours
(c)VIVADO
(d)Ours

## Slide 20: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 21: Legalization
Greedy window-based cell by cell legalization process
  Start from a small window
  Sites inside a window are consider to have same displacement
  Sort the sites by an objective function (HPWL)
  If cannot be legalized, slowly increase the window size until it’s legalized
  Keep BLEs intact unless cannot be legalized

## Slide 22: Overview of Our Algorithm
Partitioning
Packing
Routability-Driven Global Placement
Legalization
Routability-Driven Detailed Placement

## Slide 23: Detailed Placement
Move to optimal region to optimize HPWL
  In both BLE level and CLB level
  In CLB level, if the site is occupied, swap the cells if the HPWL does not increase
  In BLE level, the BLE can only be moved to a slice if it won’t violate legalization rules
CLB
BLE
BLE

## Slide 24: Detailed Placement
If already in optimal region, move to site to optimize alignment(BLE level).
  Compute the score of each site by assuming the cell is moved to there and get the alignment score by considering all related nets
  Sort the candidate sites by their alignment score, try to move the cell to a site with smaller score
(a)score=5
(b) score=4
(c) score=3
(d) score=2
(e) score=1
Comparison of alignment of different placement

## Slide 25: Experimental Result
Comparison of wirelength and runtime of our placer and the top3 winners
Design | Ours |  |  | 1st Place |  |  | 2nd Place |  |  | 3rd Place |  | 
 | WL | Time(s) | Normalized WL | WL | Time(s) | Normalized WL | WL | Time(s) | Normalized WL | WL | Time(s) | Normalized WL
FPGA-1 | 362563 | 74 | 1 | - | - | - | 379932 | 118 | 1.048 | 581975 | 97 | 1.605
FPGA-2 | 677563 | 167 | 1 | 677877 | 435 | 1.000 | 679878 | 208 | 1.003 | 1046859 | 191 | 1.545
FPGA-3 | 3617466 | 1037 | 1 | 3223042 | 1527 | 0.891 | 3660659 | 1159 | 1.012 | 5029157 | 862 | 1.390
FPGA-4 | 6037293 | 621 | 1 | 5628519 | 1257 | 0.932 | 6497023 | 1449 | 1.076 | 7247233 | 889 | 1.200
FPGA-5 | 10455204 | 1012 | 1 | 10264769 | 1266 | 0.982 | - | - | - | - | - | -
FPGA-6 | 6960037 | 2772 | 1 | 6330179 | 2920 | 0.910 | 7008525 | 4166 | 1.007 | 6822707 | 8613 | 0.980
FPGA-7 | 10248020 | 2170 | 1 | 10236827 | 2703 | 0.999 | 10415871 | 4572 | 1.016 | 10973376 | 9196 | 1.071
FPGA-8 | 8874454 | 1426 | 1 | 8384338 | 2645 | 0.945 | 8986361 | 2942 | 1.013 | 12299898 | 2741 | 1.386
FPGA-9 | 12954350 | 2683 | 1 | - | - | - | 13908997 | 5833 | 1.074 | - | - | -
FPGA-10 | 8564363 | 5555 | 1 | - | - | - | - | - | - | - | - | -
FPGA-11 | 11226088 | 3636 | 1 | 11091383 | 3227 | 0.988 | 11713479 | 7331 | 1.043 | - | - | -
FPGA-12 | 8928528 | 9748 | 1 | 9021768 | 4539 | 1.010 | - | - | - | - | - | -

## Slide 26: Experimental Result
Comparison of wirelength of different method used in our placer
Design | Raw |  | With congestion-driven GP |  | With partitioning |  | With Both | 
 | WL | Normalized WL | WL | Normalized WL | WL | Normalized WL | WL | Normalized WL
FPGA-1 | 362563 | 1.000 | 364143 | 1.004 | 378029 | 1.043 | 377883 | 1.042255
FPGA-2 | 681418 | 1.000 | 677563 | 0.994 | 696417 | 1.022 | 689360 | 1.011655
FPGA-3 | 4027586 | 1.000 | 3999517 | 0.993 | 3645846 | 0.905 | 3617466 | 0.898172
FPGA-4 | 6037293 | 1.000 | 6087199 | 1.008 | 6265158 | 1.038 | 6357766 | 1.053082
FPGA-5 | - | - | - | - | - | - | 10455204 | -
FPGA-6 | 7801736 | 1.000 | 7723476 | 0.990 | 7016684 | 0.899 | 6960037 | 0.892114
FPGA-7 | 10248020 | 1.000 | 10615672 | 1.036 | 10338763 | 1.009 | 10580828 | 1.032475
FPGA-8 | 9171179 | 1.000 | 9392039 | 1.024 | 8874454 | 0.968 | 9013564 | 0.982814
FPGA-9 | 12954350 | 1.000 | 13437554 | - | - | - | 13834692 | 1.067957
FPGA-10 | - | - | 10372369 | - | 8782789 | - | 8564363 | -
FPGA-11 | - | - | - | - | 11226088 | - | 11688504 | -
FPGA-12 | - | - | 10286583 | - | - | - | 8928528 | -

## Slide 27: Thanks